# Module 1:   Introduction

## What is an operating system?

## Simple Batch Systems

## Multiprogramming Batched Systems

## Time-Sharing Systems

## Personal-Computer Systems

## Parallel Systems

## Distributed Systems

## Real -Time Systems

# What is an Operating System?

## A program that acts as an intermediary between a user of a computer and the computer hardware.

## Operating system goals:

### Execute user programs and make solving user problems easier.

### Make the computer system convenient to use.

## Use the computer hardware in an efficient manner.

# Computer System Components

## 1.	Hardware – provides basic computing resources (CPU, memory, I/O devices).

## 2.	Operating system – controls and coordinates the use of the hardware among the various application programs for the various users.

## 3.	Applications programs – define the ways in which the system resources are used to solve the computing problems of the users (compilers, database systems, video games, business programs).

## 4.	Users (people, machines, other computers).

# Abstract View of System Components

# Operating System Definitions

## Resource allocator – manages and allocates resources.

## Control program – controls the execution of user programs and operations of I/O devices .

## Kernel – the one program running at all times (all else being application programs).

# Simple Batch Systems

## Hire an operator

## User ( operator

## Add a card reader

## Reduce setup time by batching similar jobs

## Automatic job sequencing – automatically transfers control from one job to another.  First rudimentary operating system.

## Resident monitor

### initial control in monitor

### control transfers to job

### when job completes control transfers back to monitor

# Memory Layout for a Simple Batch System

# Control Cards

## Problems

### 1.	How does the monitor know about the nature of the job (e.g., Fortran versus Assembly) or which program to execute?

### 2.	How does the monitor distinguish 
(a) job from job?
(b) data from program?

## Solution

### Introduce control cards

## Special cards that tell the resident monitor which programs to run
$JOB
$FTN
$RUN
$DATA
$END

## Special characters distinguish control cards from data or program cards:
$ in column 1
// in column 1 and 2
709 in column1

# Control Cards (Cont.)

## Parts of resident monitor

### Control card interpreter – responsible for reading and carrying out instructions on the cards.

### Loader – loads systems programs and applications programs into memory.

### Device drivers – know special characteristics and properties for each of the system’s I/O devices.

## Problem:  Slow Performance – I/O and CPU could not overlap ; card reader very slow.

## Solution:  Off-line operation – speed up computation by loading jobs into memory from tapes and card reading and line printing done off-line.

# Spooling (Multiprogrammed Batch Systems)

## Overlap I/O of one job with computation of another job.  While executing one job, the OS.

### Reads next job from card reader into a storage area on the disk (job queue).

### Outputs printout of previous job from disk to printer.

## Job pool – data structure that allows the OS to select which job to run next in order to increase CPU utilization.

# Multiprogrammed Batch Systems

- Several jobs are kept in main memory at the same time, and the CPU is multiplexed among them.

# OS Features Needed for Multiprogramming

## I/O routine supplied by the system.

## Memory management – the system must allocate the memory to several jobs.

## CPU scheduling – the system must choose among several jobs ready to run.

## Allocation of devices.

# Time-Sharing Systems–Interactive Computing

## Time-sharing or multitasking is an extension of multiprogramming; users can interact with program while it is running and many users to share the computer simultaneously.

## The CPU is multiplexed among several jobs that are kept in memory and on disk (the CPU is allocated to a job only if the job is in memory).

## A job is swapped in and out of memory to the disk.

## On-line communication between the user and the system is provided; when the operating system finishes the execution of one command, it seeks the next “control statement” not from a card reader, but rather from the user’s keyboard.

## On-line system must be available for users to access data and code.

# Personal-Computer Systems

## Personal computers – computer system dedicated to a single user.

## I/O devices – keyboards, mice, display screens, small printers.

## User convenience and responsiveness.

## Can adopt technology developed for larger operating system’

## often individuals have sole use of computer and do not need advanced CPU utilization of protection features.

# Migration of Operating-System Concepts and Features

# Parallel Systems

## Multiprocessor systems with more than one CPU in close communication.

## Tightly coupled system – processors share memory and a clock; communication usually takes place through the shared memory.

## Advantages of parallel system:

### Increased throughput

### Economical

### Increased reliability

#### graceful degradation

#### fault-tolerant systems

# Parallel Systems (Cont.)

## Symmetric multiprocessing (SMP)

### Each processor runs an identical copy of the operating system.

### Many processes can run at once without performance deterioration.

### Most modern operating systems support SMP

## Asymmetric multiprocessing

### Each processor is assigned a specific task; master processor schedules and allocates work to slave processors.

### More common in extremely large systems

# Symmetric Multiprocessing Architecture

# Real-Time Systems

## There are rigid time requirements on the operation of a processor or the flow of data.

- Often used as a control device in a dedicated application such as controlling scientific experiments, medical imaging systems, industrial control systems, and some display systems.

## Well-defined fixed-time constraints. Processing must be done within the constrained.

## Hard real-time system.

### Guarantees that critical tasks be completed on time

### Secondary storage limited or absent, data stored in short-term memory, or read-only memory (ROM)

### Conflicts with time-sharing systems, not supported by general-purpose operating systems

## Soft real-time system

### A critical task gets priority over other tasks, and retains the priority until it completes.

### Limited utility in industrial control or robotics

### Useful in applications (multimedia, virtual reality) requiring advanced operating-system features.

# Distributed Systems

## Distribute the computation among several physical processors.

## Loosely coupled system – each processor has its own local memory; processors communicate with one another through various communications lines, such as high-speed buses or telephone lines.

## Advantages of distributed systems.

### Resources Sharing

### Computation speed up – load sharing

### Reliability

### Communications

# Distributed Systems (Cont.)

## Network Operating System

### provides file sharing

### provides communication scheme

### runs independently from other computers on the network

## Distributed Operating System

### less autonomous environment

### gives the impression there is a single operating system controlling the network.

### The users access remote resources in the same manner as they do local resources.