# Module 2:  Computer-System Structures

## Computer System Operation

## I/O Structure

## Storage Structure

## Storage Hierarchy

## Hardware Protection

## General System Architecture

# Computer-System Architecture

# Computer-System Operation

## I/O devices and the CPU can execute concurrently.

## Each device controller is in charge of a particular device type.

## Each device controller has a local buffer.

## CPU moves data from/to main memory to/from local buffers

## I/O is from the device to local buffer of controller.

## Device controller informs CPU that it has finished its operation by causing an interrupt.

# Common Functions of Interrupts

## Interrupts transfers control to the interrupt service routine generally, through the interrupt vector, which contains the addresses of all the service routines.

## interrupt vector: the table of interrupt service routine address is stored in memory.

## Interrupt architecture must save the address of the interrupted instruction.

## Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt.

## A trap is a software-generated interrupt caused either by an error or a user request.

## An operating system is interrupt driven.

# Interrupt Handling

## The operating system preserves the state of the CPU by storing registers and the program counter.

## Separate segments of code determine what action should be taken for each type of interrupt

# Interrupt Time Line For a Single Process Doing Output

# I/O Structure

## After I/O starts, control returns to user program only upon I/O completion.

### wait instruction idles the CPU until the next interrupt

### wait loop (contention for memory access).

### At most one I/O request is outstanding at a time, no simultaneous I/O processing.

## After I/O starts, control returns to user program without waiting for I/O completion.

### System call – request to the operating system to allow user to wait for I/O completion.

### Device-status table contains entry for each I/O device indicating its type, address, and state.

### Operating system indexes into I/O device table to determine device status and to modify table entry to include interrupt.

# Two I/O methods

# Device-Status Table

# Direct Memory Access (DMA) Structure

## Used for high-speed I/O devices able to transmit information at close to memory speeds.

## Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention.

## Only one interrupt is generated per block, rather than the one interrupt per byte.

# Storage Structure

## Main memory – only large storage media that the CPU can access directly.

## Secondary storage – extension of main memory that provides large nonvolatile storage capacity.

## Magnetic disks – rigid metal or glass platters covered with magnetic recording material

### Disk surface is logically divided into tracks, which are subdivided into sectors.

### The disk controller determines the logical interaction between the device and the computer.

# Moving-Head Disk Mechanism

# Storage Hierarchy

## Storage systems organized in hierarchy.

### Speed

### cost

### volatility

## Caching – copying information into faster storage system; main memory can be viewed as a last cache for secondary storage.

# Storage-Device Hierarchy

# Hardware Protection

## Dual-Mode Operation

## I/O Protection

## Memory Protection

## CPU Protection

# Dual-Mode Operation

## Sharing system resources requires operating system to ensure that an incorrect program cannot cause other programs to execute incorrectly.

## Provide hardware support to differentiate between at least two modes of operations.

### 1.	User mode – execution done on behalf of a user.

### 2.	Monitor mode (also supervisor mode or system mode) – execution done on behalf of operating system.

# Dual-Mode Operation (Cont.)

## Mode bit added to computer hardware to indicate the current mode:  monitor (0) or user (1).

## When an interrupt or fault occurs hardware switches to monitor mode.

•Privileged instructions can be issued only in monitor mode.

# I/O Protection

## All I/O instructions are privileged instructions.

## Must ensure that a user program could never gain control of the computer in monitor mode (I.e., a user program that, as part of its execution, stores a new address in the interrupt vector).

# Memory Protection

## Must provide memory protection at least for the interrupt vector and the interrupt service routines.

## In order to have memory protection, add two registers that determine the range of legal addresses a program may access:

### base register – holds the smallest legal physical memory address.

### Limit register – contains the size of the range

## Memory outside the defined range is protected.

# A Base And A limit Register Define A Logical Address Space

# Protection Hardware

## When executing in monitor mode, the operating system has unrestricted access to both monitor and user’s memory.

## The load instructions for the base and limit registers are privileged instructions.

# CPU Protection

## Timer – interrupts computer after specified period to ensure operating system maintains control.

### Timer is decremented every clock tick.

### When timer reaches the value 0, an interrupt occurs.

## Timer commonly used to implement time sharing.

## Time also used to compute the current time.

## Load-timer is a privileged instruction.

# General-System Architecture

## Given the I/O instructions are privileged, how does the user program perform I/O?

## System call – the method used by a process to request action by the operating system.

### Usually takes the form of a trap to a specific location in the interrupt vector.

### Control passes through the interrupt vector to a service routine in the OS, and the mode bit is set to monitor mode.

### The monitor verifies that the parameters are correct and legal, executes the request, and returns control to the instruction following the system call.

# Use of A System Call to Perform I/O

# Text boxes

Asynchronous

Synchronous

set user mode

Interrupt/fault

user

monitor